## Slide 1
INTRODUCTORY CONCEPTS AND DEFINITIONS
MEG 212 Week 1 Lecture

## Slide 2
  At the end of this lecture, you will be able to,
  Discuss the importance of thermodynamics in meeting human needs
  • Identify application areas of thermodynamics
  • Discuss the differences between closed and open systems
  Define fundamental concepts used in thermodynamic analysis such as property, state and process
  Identify the difference between the macroscopic and microscopic views of thermodynamics
Lecture Learning Outcomes

## Slide 3
What is Thermodynamics?
It is the science concerned with the relations between heat and mechanical energy or work, and the conversion of one into the other
From two Greek Words
“Therme” meaning Heat
“Dynamis” meaning Motion or Power

## Slide 4
Importance of Thermodynamics?
21st Century Challenges
Using fossil fuels more effectively
Advancing renewable energy technologies
Developing more energy-efficient transportation systems, buildings and industrial practices
Mitigating global climate change, air pollution and water pollution
Engineers use principles drawn from thermodynamics and other engineering sciences which include fluid mechanics, heat & mass transfer to analyze and design devices used to meet human needs

## Slide 5
Application Areas of Engineering Thermodynamics
Combustion systems
Compressors & Pumps
Cooling of electronic equipment
Heating, ventilating and air-conditioning systems
Steam and gas turbines
Aircraft and rocket propulsion
Alternative energy systems
Automobile engines
Bioengineering applications
Biomedical applications

## Slide 6
Application Areas of Engineering Thermodynamics

## Slide 7
System, Boundary and Surrounding
For example, we may want to study a quantity of matter contained within a closed rigid-walled tank or a pipeline through which natural gas flows
The system is whatever we want to study which could be as simple as a free body diagram or as complex as an entire chemical refinery
In thermodynamics, the system is used to identify the subject of analysis

## Slide 8
System, Boundary and Surrounding
The system is distinct from the surrounding by means of a specified boundary
Everything external to the system is considered to be part of the system’s surroundings

## Slide 9
Difference between Closed and Open Systems
There are two basic kinds of system – the closed system and the open system (also called the control volume)
Closed system:
A gas in a piston-cylinder assembly
Fixed quantity of matter.
Also called control mass.
It is defined when a particular quantity of matter is under study
A closed system always contains the same matter
There can be no transfer of mass across its boundary
When a closed system does not interact with its surrounding in any way it is called an isolated system

## Slide 10
Difference between Closed and Open Systems
Open system: An automobile engine
A given region of space through which mass flows
Also called control volume

## Slide 11
How to select a System Boundary?
The system boundary needs to be carefully specified before any thermodynamic analysis
The choice of a system boundary is governed by two considerations
What is known about a possible system at its boundaries
The objective of the analysis

## Slide 12
Macroscopic Versus Microscopic View of Thermodynamics
Microscopic view
Sometimes called statistical thermodynamics
Objective is to characterize by statistical means the average behavior of particles making up the system of interest
Macroscopic view
Sometimes called classical thermodynamics
Concerned with the gross or overall behavior of the system
For this course, we are adopting the macroscopic view point

## Slide 13
Property, State and Process
State
Refers to the condition of a system described by its properties.
When any of the properties of the system changes, the state changes and the system is said to undergo a process
Property
Is a macroscopic characteristic of a system such as mass, volume, energy, pressure, and temperature to which a numerical value can be assigned at a given time without knowledge of the previous behavior of the system
To describe a system and predict its behavior requires knowledge of the system properties and how they are related

## Slide 14
Property, State and Process
Extensive and Intensive Properties
Extensive: depend on the size of the system e.g. mass, volume, energy etc.
Intensive: values are independent of the size of the system e.g. specific volume, pressure, temperature etc.
Process
Is a transformation from one state to another.
If a system exhibits the same values of its properties at two different times, it is in the same state at these times.
If none of the properties change with time then the system is said to be at steady state
A quantity is a property if and only if its change in value between two states is independent of the process.

## Slide 15
Equilibrium
To test for thermodynamic equilibrium
Isolate the system from its surroundings
Watch for changes in its observable properties
If there are no changes, it is concluded
Several types of equilibrium must exist individually to fulfill the condition of complete equilibrium
Mechanical, Thermal, Phase, Chemical

## Slide 16
SUMMARY
1
2
3
4
5
6
Definition
Application Areas
Importance
Macroscopic and Microscopic Views
System
Boundary
Surrounding
Property
State
Process

## Slide 17
  Reading assignment: pages 11 to 14, 18/19 to 22
  Measuring Mass, Length and Time: S.I Units and British Metric Units
  Rankine and Kelvin Temperature scales
  Celcius and Fahrenheit scales
  Engineering Design
Next Lecture